## Slide 1: The re-definition of the kelvin Why you should care, but not worry Michael de Podesta
EMPRESS Workshop
18 April 2018
Notes: NPL is highlighted on this slide to remind me to mention it upfront & always.

## Slide 2
Measurement and the SI
The redefinition of the SI
The redefinition of the kelvin
Why has this taken so long!
Consequences
Why this matters
The re-definition of the kelvin
Notes: 2

## Slide 3
It is measurement that makes science scientific. Not Maths.
Notes: 3

## Slide 4
…of an unknown quantity
with a standard quantity
Measurement is…
Quantitative Comparison
Standard
Unknown
Notes: 4
Frequently the standards are not available.
The aim of metrology is to enables accurate comparisons even when the standards are not immediately available.
The standards of the International System of units (The SI) are in practice, humanity’s choice of measurement standards.
The multiple steps could be calibrations steps for a voltmeter.
For a radiation dose measurement some of the comparisons could be with ionization chambers and some with calorimeters.

## Slide 5
Measurement is…
Quantitative Comparison
Standard
Unknown
Grade #1 Copy
Grade #2 Copy
Grade #3 Copy
Time
&
Distance
More Time
&
Distance
Even More Time
&
Distance
Notes: 5
The key point here is that the perfection of a standard quantity represents a limit to how well anything can be measured.
SI represents that limit

## Slide 6
The International System of Units
second
metre
kilogram
candela
mole
ampere
kelvin
Notes: A nice big picture of the SI roundel

## Slide 7
Measurement and the SI
The redefinition of the SI
The redefinition of the kelvin
Why has this taken so long!
Consequences
Why this matters
The re-definition of the kelvin
Notes: 7

## Slide 8
…of an unknown quantity
with a standard quantity
Measurement is…
Quantitative Comparison
Standard
Unknown
Could we choose our standards more wisely?
Notes: 8
This is the question behind the re-definition

## Slide 9
SI Base Units and Natural Constants
measure
realise
Unit Definitions
in terms of
Unit Definitions
Natural Constants
Notes: 9
Using the human based standards of the SI, we have measured natural features of the universe that appear to be constant: Natural Constants
Note: The phrase ‘natural constants’ has been carefully chosen. Avoid the use of ‘fundamental’ constants – they are not all fundamental.
Natural Constants appear to be more stable than ANYTHING human made – more later – they appear to be at least one million times more stable than the most stable human artefact – the kilogram.
The idea of the unit re-definitions is to base our system of units on these natural constants.

## Slide 10
Measurement is…
Quantitative Comparison
Standard
Unknown
Grade #1 Copy
Grade #2 Copy
Grade #3 Copy
Time
&
Distance
More Time
&
Distance
Even More Time
&
Distance
Definition
Realisation
Notes: 10
This harks back to the earlier diagram showing how the constants are ‘abstracted’ and should never change.

## Slide 11
SI. The International System of Units
Administered from BIPM
  International Bureau of Weights & Measures
Run by the CIPM
International Committee for Weights & Measures
Agenda set by the CGPM
General Conference on Weights & Measures
Resolution 1: CGPM 2014
…Encourages continued efforts to determine h, e, k, and NA with the requisite uncertainties,
Start
Measure
Measure
Measure
Measure
Measure
Measure
Measure
Measure
Measure
STOP!
2019
2018
2017
2016
2015
2014
2013
2012
2011
2010
2008
2009
2007
Resolution 12: CGPM 2007
Recommends laboratories pursue the relevant experiments so that the International Committee can come to a view on whether it may be possible to redefine the kilogram, the ampere, the kelvin, and the mole
DRAFT Resolution A: CGPM 2018
Should decide to make the change from 20th May 2019
Notes: 11
CGPM 13th November to 16th November 2018

## Slide 12
The New International System of Units
Notes: Graphical illustration of the way the constants are represented along with the units in the logo.

## Slide 13
Measurement and the SI
The redefinition of the SI
The redefinition of the kelvin
Why has this taken so long!
Consequences
Why this matters
The re-definition of the kelvin
Notes: 13

## Slide 14
In the SI one kelvin is…
…the fraction ​1⁄273.16 of the thermodynamic temperature of the triple point of water
In other words, it is defined such that the triple point of water is exactly 273.16 K exactly. i.e. 273.160 000 000 ….

## Slide 15
A triple point of water ‘cell’
Glass vessel
1. Fill with ‘water’
2. Remove the air
3. Seal
4. Water Vapour fills the space
5. Chill the middle
6. Leave to equilibrate
273.16 K
Liquid Water
Water Vapour
Solid Water
All co-exist in equilibrium

## Slide 16
The definition of the kelvin…
…makes no reference to energy…
…yet we know that temperature is a measure of the average molecular energy

## Slide 17
Molecular Motion
Thermal Physics
Triple Point of Water
Boltzmann Constant
(joules per kelvin)
Exact

## Slide 18
Molecular Motion
Thermometer
How do we relate the number produced by a thermometer (e.g. 20 °C) to the basic physics describing the jiggling of molecules?
Rock
Thermal Physics

## Slide 19
Re-defining the kelvin
‘Energy per degree’,
Boltzmann constant, kB
measure
realise
Unit Definition:
kelvin
Unit Definition in terms of the
Notes: 19

## Slide 20
Measurement and the SI
The redefinition of the SI
The redefinition of the kelvin
Why has this taken so long!
Consequences
Why this matters
The re-definition of the kelvin
Notes: 20

## Slide 21
Jean-Baptiste Joseph Fourier (1807 - 1820)
  Breathtaking mathematical progress
  Distinction between thermal and mechanical quantities
Anders Celsius (1710) and Daniel Gabriel Fahrenheit (1724)
  Allowed people to investigate the world
  Thermometers were useful
Henri Victor Regnault (1840s)
  Established the superiority of the ‘air thermometer’ (CVGT)
Thermal pioneers
John Tyndall (1865)
  Wrote the textbook: “Heat: a mode of motion”
John James Waterston (1845)
  Theory of Free and Perfectly Elastic Molecules in a State of Motion
John Baptiste Perrin (1926)
  Nobel prize for finally demonstrating the existence of atoms
James Clerk Maxwell (1859-1866)
Ludwig Boltzmann (1866)
Josiah Willard Gibbs(1901)
  The kinetic theory of gases
No consensus on what thermometers measured!

## Slide 22
Newton comprised the system of the universe. It is recognised that the same principles regulate all the movements of the stars, their form, the inequalities of their courses, the equilibrium and oscillations of the seas, the harmonic vibrations of the air and sonorous bodies, the transmission of light, capillary actions, the undulations of fluids…
But whatever may be the range of mechanical theories, they do not apply to the effects of heat. These make up a special order of phenomena which cannot be explained by the principles of motion and equilibrium.
Preliminary
Discourse
Jean Baptiste Joseph Fourier
Analytical Theory of Heat
Notes: By Original uploader was User:Bunzil at en.wikipedia - Originally from en.wikipedia; description page is/was here., Public Domain, https://commons.wikimedia.org/w/index.php?curid=3308441

## Slide 23
John James Waterston (1845)
On the Physics of Media that are Composed of Free and Perfectly Elastic Molecules in a State of Motion

## Slide 24
Pages 6 & 7
…we must imagine a vast multitude of small particles of matter, perfectly alike in every respect
…The quality of perfect elasticity being common to all the particles, the original amount of vis viva …of the whole multitude must forever remain the same… as unchanged as the matter that is associated with it.
The medium must in this way become endowed with a permanent state of elastic energy, or disposition to expand, uniformly sustained in every part and communicating to it the physical character of an elastic fluid.
“The paper is nothing but nonsense”
Referee 1845
“The omission to publish it at the time was a misfortune which probably retarded the subject by 10 to 15 years.”
Commentary by Lord Rayleigh in 1896

## Slide 25
John Tyndall
HEAT: a Mode of Motion 1865
In the following Lectures I have endeavoured to bring the rudiments of a new philosophy within the reach of a person of ordinary intelligence and culture.
The first seven Lectures of the course deal with thermometric heat; its generation and consumption in mechanical processes; the determination of the mechanical equivalent of heat; the conception of heat as molecular motion; the application of this conception to solid, liquid and gaseous forms of matter; to expansion and combustion; to specific and latent heat and to calorific conduction..
Notes: By Original uploader was User:Bunzil at en.wikipedia - Originally from en.wikipedia; description page is/was here., Public Domain, https://commons.wikimedia.org/w/index.php?curid=3308441

## Slide 26
Josiah Willard Gibbs
Elementary Principles in Statistical Mechanics 1901
In the present state of science, it hardly seems possible to frame a dynamic theory of molecular action…
Even if we confine our attention to the phenomena distinctively thermodynamic, we do not escape difficulties in as simple a matter as the number of degrees of freedom of a diatomic gas. It is well known that while theory would assign to the gas six degrees of freedom per molecule, in our experiments on specific heat we cannot account for more than five. Certainly, one is building on an insecure foundation who rests his work on hypotheses concerning the constitution of matter.
Notes: By Original uploader was User:Bunzil at en.wikipedia - Originally from en.wikipedia; description page is/was here., Public Domain, https://commons.wikimedia.org/w/index.php?curid=3308441

## Slide 27
Jean Baptiste Perrin
Nobel Prize for Physics 1926
“for his work on the discontinuous structure of matter, and especially for his discovery of sedimentation equilibrium”.
The discovery of such relationships marks the point where the underlying reality of molecules becomes a part of our scientific consciousness.
Notes: By Original uploader was User:Bunzil at en.wikipedia - Originally from en.wikipedia; description page is/was here., Public Domain, https://commons.wikimedia.org/w/index.php?curid=3308441
http://www.britannica.com/biography/Jean-Perrin

## Slide 28
Now our ideas are clearer…
And we have progressed experimentally…
Notes: 28
The definition of the kelvin in the new SI: its rationale, implementation and implications

## Slide 29
We have (slowly) got better at measuring kB
From White and Fischer: Metrologia 52 (2015) S213-S216
Relative uncertainty in the Boltzmann constant
Relative reproducibility of practical temperature scales at ~ 100 °C
Notes: 29
The definition of the kelvin in the new SI: its rationale, implementation and implications

## Slide 30
Temperature measurement became important for science and engineering before we understood what we were measuring!
Why has this taken so long?

## Slide 31
Measurement and the SI
The redefinition of the SI
The redefinition of the kelvin
Why has this taken so long!
Consequences
Why this matters
The re-definition of the kelvin
Notes: 31

## Slide 32
Consequences
The redefinition of the kelvin is not intended to solve an existing problem.
The intention is to ‘lay foundations’ for possible future improvements.
For anyone who use the International Temperature Scale of 1990.
There are no consequences arising from the redefinition.
Notes: 32
CGPM 13th November to 16th November 2018

## Slide 33
Molecular Motion
Thermal Physics
Triple Point of Water
Boltzmann Constant
(joules per kelvin)
Exact

## Slide 34
Possible future improvements
A measurement at 1500 °C
Now: Every temperature measurement is a comparison against the temperature of the triple point of water.
Pyrometer Measurement
Compares brightness at unknown temperature with brightness at (say) freezing temperature of silver
Freezing temperature of silver estimated using constant volume gas thermometry or Johnson noise thermometry in terms of the triple point of water.
In the future: Every temperature measurement is a comparison of molecular energies with the Boltzmann constant.
Pyrometer Measurement
Compares brightness at unknown temperature with the Planck formula
Notes: 34
CGPM 13th November to 16th November 2018

## Slide 35
Possible future improvements
A measurement at 1500 °C
Now: Every temperature measurement is a comparison against the temperature of the triple point of water.
Pyrometer Measurement
Compares brightness at unknown temperature with brightness at (say) freezing temperature of silver
Freezing temperature of silver is estimated using constant volume gas thermometry or Johnson noise thermometry in terms of the triple point of water.
In the future: Every temperature measurement is a comparison of molecular energies with the Boltzmann constant.
Pyrometer Measurement
Measure absolute radiant intensity of source (Planck formula)
Johnson Noise Measurement
Measure absolute value of electrical noise
Notes: 35
CGPM 13th November to 16th November 2018

## Slide 36
Measurement and the SI
The redefinition of the SI
The redefinition of the kelvin
Why has this taken so long!
Consequences
Why this matters
The re-definition of the kelvin
Notes: 36

## Slide 37
…brings the world into focus
Precision Measurement…

## Slide 38: Thank you:
The National Physical Laboratory is operated by NPL Management Ltd, a wholly-owned company of the Department for Business, Energy and Industrial Strategy (BEIS).

## Slide 39
Extra Slide
Notes: 39

## Slide 40
The second
The unperturbed ground state
hyperfine transition frequency
of the caesium 133 atom
Notes: The second is definition terms of the Delta nu-133

## Slide 41
The second
We measure time by counting a periodic phenomenon
Historically
The orbit of the Earth around the Sun
​1 second = 1⁄31,556,925.9747 of the year 1900
In the SI
The oscillation of an atom of Caesium-133
= 9,192,631,770 oscillations per second
One second is 9,192,631,770.000 000… oscillations

## Slide 42
The metre
The speed of light in vacuum, c
The unperturbed ground state
hyperfine transition frequency
of the caesium 133 atom

## Slide 43
The metre
We measure distance by using a ‘standard length’
Historically
A standard fraction of the Earth’s size
In the SI...
The speed of light c in a vacuum is a fundamental universal constant
Fixing c = 299,792,458 metres per second exactly defines 1 metre
We measure distances in terms of
In practice...
For light of a given frequency (colour) the wavelength is fixed
We can count wavelengths of light using an interferometer.
10,000,000 m
MIRROR
LASER

## Slide 44
The kilogram
The Planck constant, h
The speed of light in vacuum, c
The unperturbed ground state
hyperfine transition frequency
of the caesium 133 atom

## Slide 45
The kilogram
N
N
S
Historically
The weight of standard container of water
In the SI currently…
International Prototype of the Kilogram
Force of gravity balanced by comparison with standard mass
In the New SI…
Force of gravity balanced by comparison with magnetic force
Calculable in terms of
10 cm
10 cm
10 cm
= 1 kg

## Slide 46
The ampere
The elementary charge, e
The unperturbed ground state
hyperfine transition frequency
of the caesium 133 atom

## Slide 47
Historically
the current that would deposit 1.118 milligrams of silver per second from a silver nitrate solution.
The ampere
In the SI currently…
Defined by force between parallel wires
Actually force between coils
In the New SI…
A number of electrons per second
e = 1.602176634×10−19 C
Current calculable in terms
1 metre

## Slide 48
Historically
the current that would deposit 1.118 milligrams of silver per second from a silver nitrate solution.
The ampere
A
Notes: 1 ampere = 1 C/s
1 C = 1/1.6e-19 electrons
= 1/1.6e-19 atoms of silver
1 atom of silver = 107.87 g/ NA
Mass per second = 107.87 /(1.6e-19 * NA)
= 1.12 mg/s

## Slide 49
The ampere
In the SI currently…
Defined by force between parallel wires
Actually force between coils
1 metre
A
Notes: 1 ampere = 1 C/s
1 C = 1/1.6e-19 electrons
= 1/1.6e-19 atoms of silver
1 atom of silver = 107.87 g/ NA
Mass per second = 107.87 /(1.6e-19 * NA)
= 1.12 mg/s

## Slide 50
The ampere
In the New SI…
V measured using Josephson effect in multiples of KJ = h/2e
R measured using Quantum Hall Effect in multiples of KVK = h/e2
Ratio V/R yields currents calculable in terms of
e = 1.602176634×10−19 C
A
Resistor
V
In the SI currently…
Defined by force between parallel wires
Actually force between coils
Notes: 1 ampere = 1 C/s
1 C = 1/1.6e-19 electrons
= 1/1.6e-19 atoms of silver
1 atom of silver = 107.87 g/ NA
Mass per second = 107.87 /(1.6e-19 * NA)
= 1.12 mg/s

## Slide 51
Defining constants
Notes: Q: What is the difference between the MKSA (metre-kilogram-second-ampere) system of units and the SI
A: No difference really, but the SI has ‘people who care’
People who care are rare 1000 in 7 billion ~ 1 in 7 million ~ 1 pixel on this screen
This is the existing arrangement: Looks pretty but does not show structure

## Slide 52
Defining constants
second,
Constant of nature. But we could have chosen other atoms
metre,
c appears to be a universal and fundamental constant of nature
kilogram,
h appears to be a universal and fundamental constant of nature
ampere,
e appears to be a universal and fundamental constant of nature
MKSA would be sufficient to define a system of units.
  SI is not designed to be a ‘minimal’ system
  It has been constructed to respond to human requirements
  measured to be at least one million times more stable than the kilogram!

## Slide 53
The kelvin
The Boltzmann constant, k
The Planck constant, h
The unperturbed ground state
hyperfine transition frequency
of the caesium 133 atom

## Slide 54
The kelvin
Historically
We did not know what temperature was until long after we learned to measure it!
In the SI currently…
A single ‘standard temperature’
The temperature of the triple point of water is 273.160 000 … K
In the New SI…
Boltzmann constant 1.380 648 52 x 10-23 J K-1
Stating the temperature in kelvin is equivalent to stating the average molecular energy in terms of

## Slide 55
The candela
the luminous efficacy of monochromatic radiation of frequency 540×1012 Hz, Kcd
The Planck constant, h
The unperturbed ground state
hyperfine transition frequency
of the caesium 133 atom
Notes: The luminous efficacy Kcd is a technical constant that gives an exact numerical relationship between the purely physical characteristics of the radiant power stimulating the human eye (W) and its photobiological response defined by the luminous flux due to the spectral responsivity of a standard observer (lm) at a frequency of 540×1012 hertz

## Slide 56
The candela
The unit of luminous intensity
How bright do lights appear to humans?
The only SI unit based on human perception
Historically
Based on Standard Candles – hence the name
In the SI
Defined at one colour – green light with a wavelength of 555 nm
This is close to the peak sensitivity of the human eye
1/683 watt per steradian

## Slide 57
The mole
The Avogadro constant

## Slide 58
The mole
Historically
Links chemical measurements to the SI
The Avogadro number of elementary entities, usually atoms or molecules
In the SI currently…
The number of atoms in 12 g of 12C.
Defined by weighing
In the New SI…
Avogadro constant defined exactly
NA= 6.022140857×1023 mol−1.
Defined exactly: Realised by weighing
1 mole of lead
1 mole of copper
18.27 cm3
22,400 cm3
1 mole of oxygen molecules
7.09 cm3

## Slide 59
Defining constants

## Slide 60
Defining constants
kelvin, ,
The Boltzmann, k, constant is a scaling constant
It relates temperature to molecular energy
candela, Kcd
The candela constant Kcd is a technical constant
Sensitivity to light actually varies from one person to another
mol,
The Avogadro constant NA is a scaling constant
It relates moles to numbers of elementary entities
SI has been constructed to respond to human requirements

## Slide 61
Defining constants

## Slide 62
The Power of Measurement
Measurement and the SI
The redefinition of the SI
Details of the SI base units
Brand new bright tomorrow
The Power of Measurement
Notes: 62

## Slide 63
KRISS
NMIJ
User 2
User 1
User 3
Calibration Lab
NPL
NIST
PTB
LNE-CNAM
NIM
International Bureau of Weights and Measures, BIPM
Traceability